## Slide 1: Indoor Proximity Based Advertising Using Bluetooth Beacons by Finn Zhan Chen

## Slide 2: System Structure Overview

## Slide 3: Data Collection And Cloud Storage

## Slide 4: IoT Device Firmware
Scan for advertisements
Filter advertisements
Combine MAC and RSSI
Update custom characteristic
Notifies the subscribed device
nRF51-DK

## Slide 5: Gateway Android App
Subscribe to IoT device via Bluetooth
Receives notifications
Decodes data
Post data to Cloud via WiFi

## Slide 6: The Localisation Algorithm

## Slide 7: Beacon’s proximity to the IoT device
RSSI is the radio signal strength indicator in dBm
n is the signal propagation constant (n=2 in free space)
d is the proximity to beacon
A is a reference RSSI in dBm (RSSI at 1 metre from beacon)

## Slide 8: Getting the Reference RSSI (Calibration)
50 RSSIs collected at roughly 1 metres from each beacon.
The noises filtered by removing the outliers.
Averaged to get the reference RSSI.

## Slide 9: Calculating Proximity Using RSSI
At the time of localisation, the RSSI collected in the past t seconds will be used (t is the data time window).
Noises are filtered by removing outliers.
The mean of the RSSIs is used in the equation.

## Slide 10: 3D Trilateration
Existing Python package for trilateration.
Uses geographic coordinate system (lat and lng)
Weakness:
  requires exactly 3 beacons.
  must have mutual intersecting points.

## Slide 11: 2D Trilateration
Uses cartesian coordinate system(x and y)
Universal Transverse Mercator (UTM) coordinates
Strength:
  works with 2 or more beacons
Weakness:
  must have mutual intersecting points.

## Slide 12: Generalised 2D Lateration
Code modified
Get centre of all intersecting points
Weight based approach
  Normal intersecting points weigh 1x
  Mutual intersecting points weigh 2x

## Slide 13: Generalised 2D Lateration: Additional Features
Filter discovered beacons >10 metres
Last estimated location as a beacon (If within the past 5s and radius increases 0.5m/s assuming the user moves 0.5m/s)
Estimated location optimisation (Finding X that minimises mean squared error)

## Slide 14: Visualisation

## Slide 15: Android App Visualisation

## Slide 16: Cloud Dashboard: Homepage

## Slide 17: Cloud Dashboard: Path Trace

## Slide 18: Cloud Dashboard: Path Reconstruction

## Slide 19: Cloud Dashboard: Heatmap

## Slide 20: Performance Evaluation

## Slide 21: Test Setup

## Slide 22: Result
Time at each Test Point: 30s
Time Window for Data: 4.5s
Time Window for Algorithm: 3s
Number of estimated location: 112
Test Point: 0 Number of Estimated Locations: 8 Mean Distance Error: 3.1570353838851464
Test Point: 1 Number of Estimated Locations: 5 Mean Distance Error: 1.0454290095323688
Test Point: 2 Number of Estimated Locations: 6 Mean Distance Error: 3.867109226134572
Test Point: 3 Number of Estimated Locations: 3 Mean Distance Error: 4.209911370221693
Test Point: 4 Number of Estimated Locations: 6 Mean Distance Error: 2.550590978083412
Test Point: 5 Number of Estimated Locations: 6 Mean Distance Error: 4.659396844781046
Test Point: 6 Number of Estimated Locations: 3 Mean Distance Error: 2.641241776631099
Test Point: 7 Number of Estimated Locations: 10 Mean Distance Error: 5.735763376893904
Test Point: 8 Number of Estimated Locations: 6 Mean Distance Error: 3.553800402363198
Test Point: 9 Number of Estimated Locations: 7 Mean Distance Error: 5.096912579179528
Test Point: 10 Number of Estimated Locations: 11 Mean Distance Error: 3.244255123105696
Test Point: 11 Number of Estimated Locations: 9 Mean Distance Error: 2.6440261327014656
Test Point: 12 Number of Estimated Locations: 8 Mean Distance Error: 1.3556790824841536
Test Point: 13 Number of Estimated Locations: 4 Mean Distance Error: 2.233608023472335
Test Point: 14 Number of Estimated Locations: 6 Mean Distance Error: 4.753636728148626
Overall Mean Distance Error: 3.3832264025078826 metres
Notes: The localisation algorithm on average provides an accuracy of 3.38 metres. The results for the test points provides 1 to 6 metres accuracy depending on environment factors such as wall, furniture, and distribution of the Bluetooth beacons.

## Slide 23: Result Visualised
Notes: As clearly shown in blue line in Fig, the localisation algorithm is heavily dependent on the Bluetooth beacons and is limited within the blue lines. Limitations: heavility reliant on RSSI, not additional sensors

## Slide 24: Conclusion & Use Cases

## Slide 25: Thanks for Listening